## Slide 1
Handling Execution
Overruns
Hard real-time control systems • CBS/CBShd • Prototype simulation
Christian Percival
Electronic Engineering • Hochschule Hamm-Lippstadt
Core question
How can a hard real-time system stay safe when a task suddenly needs more execution time than expected?

## Slide 2
Why execution overruns matter
Hard real-time is not just “fast” — it must be predictable.
Hard deadline risk
A late result can be useless or dangerous in control systems. Correct value + wrong time = wrong behavior.
WCET-only scheduling
Safe but often pessimistic: reserves time for the rare worst case every cycle, lowering normal-case performance.
Variable execution time
Vision, tracking, and sensor processing often run fast normally but become expensive in exceptional cases.
Unsafe if overruns are ignored
Inefficient if always WCET
Goal: bounded adaptation
Execution overrun = actual runtime exceeds the expected/reserved budget, not simply finishing below WCET.
Refs: Caccamo, Buttazzo & Sha (2002); Buttazzo, Hard Real-Time Computing Systems (2024).

## Slide 3
Motivating example: visual tracking
Normal frames are cheap; difficult frames force larger search regions.
Synthetic image frame
small
predicted
window
object
1. Small window
fast normal case
2. Medium window
partial overrun
3. Full image
worst case
Overrun behavior is input-dependent
The difficult input does not change the task identity — it changes how much work the task must do before it can produce the control result.
Main paper motivation: variable visual tracking/search window execution time.

## Slide 4
What exactly is an overrun?
The task exceeds its normal/reserved execution budget.
time
normal runtime cn
overrun
deadline
Normal job
Overrun job
Key relation
Actual execution time:
ci > cin
Overrun amount:
ci − cin
WCET remains the safety bound, but using WCET for every job can waste bandwidth when overruns are rare.
Notation: ci = actual execution time, cin = normal computation time.

## Slide 5
Three scheduling strategies to compare
This structure is useful for the implementation and the final paper.
1. WCET-based
Reserve worst-case time for every job.
✓ strong safety if WCET is correct
✕ wasted CPU in normal cases
2. Normal-budget only
Reserve normal execution time only.
✓ high normal-case frequency
✕ overruns can cause deadline misses
3. Overrun-handled
Reserve normal budget, but detect and account for extra execution with a deadline/bandwidth rule.
✓ balances efficiency and protection
The prototype should show the tradeoff visually: safe-but-slow vs fast-but-unsafe vs adaptive-with-bounds.

## Slide 6
Rate adaptation and control performance
Higher control frequency improves response, but consumes more CPU.
Performance Loss Index
ΔJi(fi) = αi e−βi fi
• fi = task / sampling frequency
• αi = magnitude of loss
• βi = decay rate
• lower ΔJ means better control
performance loss ΔJ
frequency fi
as frequency increases, loss decreases
Rate adaptation idea: run faster during normal cases; slow or postpone only when bounded overruns occur.
PLI model follows Seto et al. and is used by Caccamo et al. for frequency optimization.

## Slide 7
CBS and CBShd: isolate the overrun
The overrun should mainly affect the task that caused it.
Server parameters
Budget Qs
Period Ts
Bandwidth Us = Qs/Ts
CBS behavior
1. Task consumes budget
2. Budget exhausted
3. Deadline postponed
4. Budget replenished
5. Task continues later
CBShd improvement
If remaining overrun is small, recharge only what is needed and postpone the deadline less.
less pessimistic
Temporal isolation: other tasks should not lose their guarantees because one task has a difficult input.
CBS: Abeni & Buttazzo (1998); CBShd: Caccamo, Buttazzo & Sha (2002).

## Slide 8
Prototype simulation design
A learning prototype, not a kernel-level real-time scheduler.
Generate images
easy / medium / hard / missing
Image search task
small → medium → full region
Timing log
runtime, overrun, deadline miss
Recommended: Python + NumPy/OpenCV
• Fast to build
• Easy CSV logging
• Easy plotting for final paper
• Synthetic images give controlled WCET cases
Optional formal view: UPPAAL
• Model task states
• Verify deadline properties
• Show unsafe normal-only strategy
• Better for proof than runtime plots
Prototype claim: controlled timing experiment and scheduling simulation for learning and demonstration.

## Slide 9
What the prototype should show
Expected patterns before real measurements are collected.
Runtime per frame
normal budget
Deadline misses per strategy
Chart: 
| WCET | Normal | Handled
Expected | 0 | 5 | 1
Interpretation
WCET is safe but slow; normal-only is fast but unsafe; handled scheduling should reduce uncontrolled misses and show the purpose of budget-based overrun management.

## Slide 10
Optional UPPAAL model
Use formal verification to complement the software timing demo.
Task automaton
States: Idle → NormalExec → OverrunExec → Complete / DeadlineMiss
Environment chooses easy, medium, hard, or missing input.
Server automaton
Tracks budget and deadline.
If budget is exhausted, deadline is postponed according to the handling rule.
Queries
Handled strategy:
A[] not deadline_missed
Unsafe strategy:
E<> deadline_missed
Use UPPAAL for “can a deadline miss occur?”; use Python/C++ for measured execution-time plots.

## Slide 11
Conclusion
Handling overruns balances predictability and efficiency.
Execution overruns are dangerous because one unexpectedly long task can break timing guarantees for the entire task set.
Theory
Rate adaptation, CBS, and CBShd provide a structured way to handle variable execution while keeping bounded behavior.
Prototype
Synthetic image search can demonstrate normal runtime, overrun spikes, deadline misses, and simplified handling.
Critical view
The hardest practical issues are WCET estimation, OS jitter, scheduler overhead, and shared resource blocking.
Discussion question: Would a simplified overrun handler be useful for perception-heavy embedded systems, or is WCET estimation still the bottleneck?

## Slide 12
Key references
Use these in the paper and presentation.
[1] M. Caccamo, G. Buttazzo, and L. Sha, “Handling Execution Overruns in Hard Real-Time Control Systems,” IEEE Transactions on Computers, 2002. [2] G. Buttazzo, Hard Real-Time Computing Systems: Predictable Scheduling Algorithms and Applications, 4th ed., Springer, 2024. [3] L. Abeni and G. Buttazzo, “Integrating Multimedia Applications in Hard Real-Time Systems,” RTSS, 1998. [4] C. L. Liu and J. W. Layland, “Scheduling Algorithms for Multiprogramming in a Hard-Real-Time Environment,” JACM, 1973. [5] D. Seto, J. P. Lehoczky, L. Sha, and K. G. Shin, “On Task Schedulability in Real-Time Control Systems,” RTSS, 1996. [6] T. P. Baker, “Stack-Based Scheduling of Realtime Processes,” Real-Time Systems, 1991. [7] G. Bradski, “The OpenCV Library,” Dr. Dobb’s Journal of Software Tools, 2000.
Note: Implementation results are proposed/expected until measured data are collected.